## Slide 1
Dreame technical information and rooting:
Get control over your vacuum robot
Notes: Welcome to the rooting how-to of the Dreame robots. Here I will show you how to get control over your vacuum robot

## Slide 2: Before you continue: Please look thru all slides and the FAQ before you start your adventure
All commands and FAQ can be found here:
https://builder.dontvacuum.me/dreame/
You might want to join the Telegram channel:
https://t.me/dust_announce
Notes: Before we start a few comments. Please watch the whole video before you start your adventure. If you don’t have a technical background, you might be overwhelmed with this.
All the commands we use here are linked in the description. You can copy and paste them from the cheatsheet.

## Slide 3: Good news: No soldering or teardown required

## Slide 4: Why get root access?
Use Valetudo (https://valetudo.cloud/)
  Replace the cloud functionality with an open-source software
  Integrate the device into your home automation
Install your own soundfiles/voices
Notes: Ok, lets talk why do we want to get root access in the first place.
Many users purchased their robot as the T6 model, which is geo-blocked outside of Mainland china. With root access you can remove this geo-blocking.
Probably the most important reason is to use the Valetudo software, which replaces the cloud functionality with open source software. This also enables you to integrate the device in your home automation software.
Also we can install our own soundfiles and voices.

## Slide 5: Currently tested devices (02.2022)
Xiaomi Vacuum 1C: UART*/Reset**/Livesuit
Dreame D9 (normal and Pro): UART*/Reset*/Livesuit
Dreame F9: UART*/Reset*/Livesuit
Xiaomi Vacuum 1T: Reset*/Livesuit**
Dreame L10 Pro: Reset*/Livesuit**
Dreame Z10 Pro: Reset*/Livesuit**
Mova Z500: Reset*/Livesuit**
* Method patched in new versions, check https://dontvacuum.me/robotinfo/
** Method might not be available in too old or too new versions.
*** Method likely to be patched with future firmware updates

## Slide 6: Risks
A failed flash can leave the device in an undefined state
Requires reflashing
Problem:
  All partitions need to be recreated
  Device identity (Device ID, Cloud keys, MAC) gets lost
  Calibration data lost
Observations:
  Device identity does not matter if you use Valetudo
  Unknown consequences for lost calibration data

## Slide 7: More risks
Problem: Hardware differs even for the same „model“
The root method cannot verify your exact model
Flashing an incorrect firmware will perma-damage your device
  Other, not obvious side effects might occur
  Recovery might be tricky and can cause problems
Important: Make sure that you have the correct firmware
  Do not try to use the same generated firmware on multiple devices
  If you are unsure, ask us first!

## Slide 8: Sidenotes
Rooting will permanently change files on your device*
  Cloud connection / App usage should be still possible
By installing a custom firmware, you cannot update your device with official firmwares anymore **
  That is the price of rooting
  You can update your device with custom firmwares
Connect to your robot and write down the MAC address
  * we needed to reconstruct parts from the firmware by extracting contents from flash and guessing unknown parts.
  ** if you backup the encryption keys, you can restore them at a future time. In special circumstances (dead hardware) we might provide you with stock firmware.

## Slide 9: Important information
DO NOT UPDATE THE FIRMWARE VIA THE APP if you ever plan to root your device
  New firmwares have rooting methods patched
  Root might be still possible, but is more complicated and risky
Before rooting: test the device without using the app
  Fully charge your device
  Use the buttons to start the cleaning run
  Let the robot clean multiple times
  Background: Some devices come with defects from the factory. It is tricky to figure out if your robot behaves weirdly due to it being already broken or due to rooting

## Slide 10: Current available rooting methods
UART
  Requires: UART connection
  Idea: Interrupting the bootloader, boot into single-user-mode, flash firmware
Reset (Currently recommended)
  Requires: UART connection
  Idea: trigger the secret login shell by pressing reset <=1 sec, compute root password, login, flash firmware
Livesuit
  Requires: USB connection, UART (recommended but not required)
  Idea: creation of special factory image, triggering bootrom mode (FEL), flashing of all partitions via Livesuit software (requires Windows)

## Slide 11: Tools required for root
UART-USB adapter (3.3V, aka TTL adapter)
  Typical chipsets:
    FT232RL, FT232, PL2303TA or CP2102
  Price ~10 USD/Euro
Breadboard Jumper Wires
2mm pitch headers
USB cable (for Livesuit/FEL)
  (e.g. from a broken USB mouse)
Alternative: custom PCBs
Notes: To root the devices we need a few tools. We need screwdrivers to disassemble the device. I created a step by step video about how to do that. Its linked in the description.
Also we need a UART to USB adapter. You might find them under various names, like serial adapters or TTL adapters. The important thing here is that they support 3.3V logic level. Usually you can get them very cheaply over amazon or even in local stores.
For the actual connection, we need a few thing isolated copper wires or some breadboard jumper wires. Also some tape might be helpful.

## Slide 12: Opening the device

## Slide 13: Opening the device

## Slide 14: Opening the device

## Slide 15: Opening the device

## Slide 16: Opening the device

## Slide 17: Debug pinout
Dontvacuum.me
Front
Boot_SEL
RX
TX
D+
D-
VBUS
(Do not connect)
GND
Debuginterface
  2x8 pins
  2mm pitch size
Warning:
2mm pitch size is way smaller
than the usual 2.54 mm
Warning:
Make sure you connect to the
correct pins!

## Slide 18: Rooting with custom PCBs
USB + UART headers
(aka basic PCB)
USB + integrated UART
Adapter
(aka Advanced PCB)
Check builder.dontvacuum.me/dreameadapter for the Gerber files

## Slide 19: Rooting with custom PCBs
USB + UART headers
(aka basic PCB)
USB + integrated UART
Adapter
(aka Advanced PCB)
Check builder.dontvacuum.me/dreameadapter for the Gerber files

## Slide 20: Usage of basic PCB
Front
Front
Marker
(front, right)
USB
UART
BOOT_SEL

## Slide 21: Usage of advanced PCB
Front
Front
UART
USB
USB
UART
Marker
(needs to be on the right)
BOOT_SEL
BOOT_SEL

## Slide 22: Usage of Archi’s PCB*
* Created by Telegram User Sebastian (@ArchimedesMP)
Front
Front

## Slide 23: Connecting jumper wires (2mm pitch)

## Slide 24: Reset Method

## Slide 25: Reset Method
You can find all commands and steps in a text file here:
  https://builder.dontvacuum.me/dreame/cmds-reset.txt
  It is recommended that you copy+paste the commands (instead of typing them)
Background
  The login shell is by default disabled on Dreame robots
  The developers left a hidden function:
    If reset button is pressed for <=1 second, a login shell is triggered
    The root password is computed from the device serial number
  This hidden function is patched in firmwares newer than 10.2021

## Slide 26: Reset Method Step 0
Compute the root password from the serial number
  Under Linux:
    'echo -n "P2009XXXXXXXXXXXXX" | md5sum | base64’ (where “P2….” is your serial)
    The expected result is: 'Y2QxNjA4YjdhNWU1Y2RlNGQ3ODkzZjY4Yzk1MTVkOTAgIC0K’
  Or use https://builder.dontvacuum.me/dreamepassword.php
Important:
  Use the serial under the dustbin
  Use both lines
  Serial number under the robot differs!!

## Slide 27: Reset Method Step 1
Get an adapter
Reminder: Works only on 1C/F9/D9
UART-USB adapter (3.3V, aka TTL adapter)
  Typical chipsets:
    FT232RL, FT232, PL2303TA or CP2102
  Price ~10 USD/Euro
Notes: To root the devices we need a few tools. We need screwdrivers to disassemble the device. I created a step by step video about how to do that. Its linked in the description.
Also we need a UART to USB adapter. You might find them under various names, like serial adapters or TTL adapters. The important thing here is that they support 3.3V logic level. Usually you can get them very cheaply over amazon or even in local stores.
For the actual connection, we need a few thing isolated copper wires or some breadboard jumper wires. Also some tape might be helpful.

## Slide 28: Reset Method Step 2a
Know where RX and TX on your adapter is
Configure your UART program
  Baud: 115200
  Flow control: off (!)
Test the settings without robot
Notes: In this step, we want to setup your computer for the serial connection. You need to know where the RX and TX on your adapter is. For some adapters its marked, for some it’s a particular color of cable. In my case white was RX and green was TX. But don’t worry, you cant damage your robot, if you have it wrong.
Set your UART program to 115200 baud and disable flow control. This is very important. I have shown here a few example programs. Finally you want to test your settings. If you connect TX and RX of your adapter together and then type something, you should see an echo. This is what we call loopback.

## Slide 29: Reset Method Step 2b
Power off the robot before proceeding
Remove it from the base station
Connect serial wires to PCB
  Do not connect 5V (red cable)!
  Test for correct connection
    Press the power button for 3 seconds
    You should see some output
    If you don’t see anything, try to switch RX and TX
Notes: In the next step, we connect to the robot. First, we need to connect the battery to the PCB. There is only one way to connect it, so you should not be able to do it wrong.
Then we connect the serial wires to the PCB. As mentioned before, you can use a MicroUSB cable to get ground. Connect TX and RX. Do not connect the red cable which is 5V. This is very important.
As a first test, that you did everything correctly, press the power button less than one second. It’s the middle button on the PCB. If you do that, you should see some text output from your robot. If you don’t see anything, then you might have mixed RX and TX or your connection is bad. If you see some cryptic text, your settings might be incorrect.

## Slide 30: Reset Method Step 3
Wait for the robot to boot
Press reset button for <=1sec
  The reset button is next to the WiFi LED
If you see something like “/etc/os_release”, your firmware might too new (or too old for 1C/F9/D9) 
If success full, you should see “pxxx_login:”
  enter user “root”
  enter password (that you computed in Step 0)
  You should have a shell now

## Slide 31: Reset Method Step 4
Check this document: https://builder.dontvacuum.me/dreame/cmds-reset.txt
Check the current installed version (check "fw_arm_ver"):
  cat /etc/os-release
Run these commands to print the configuration (save output):
  grep "" /mnt/private/ULI/factory/*
Run these commands to save the calibration (save output, outside of the robot):
  grep "" /mnt/misc/*.json
  grep "" /mnt/misc/*.yaml
  cat /mnt/misc/*.txt
  hexdump /mnt/misc/*.bin
Depending on your device model, some of the files might not exist for you. If you get file errors, it is totally fine and you can proceed.
Make sure that you copy the full output to a text file and save it

## Slide 32: Reset Method Step 5
Check this document: https://builder.dontvacuum.me/dreame/cmds-reset.txt
Make copies of the firmware encryption keys (e.g., to restore the robot to a factory state)
  cat /etc/OTA_Key_pub.pem
  cat /etc/publickey.pem
Make sure that you save the output of the calibration and the encryption keys before proceeding
Run these commands to create binary backups:
  mkdir -p /tmp/backup
  tar -cvzf /tmp/backup/misc_backup.tgz -C /mnt/misc .
  tar -cvzf /tmp/backup/factory.tgz -C /mnt/private/ULI/factory/ .
  cp /tmp/backup/*.tgz /data/

## Slide 33: Reset Method Step 6
Check this document: https://builder.dontvacuum.me/dreame/cmds-reset.txt
If the robot is already in your WiFi, skip this step
If the robot is still unprovisioned, you have 2 choices
  Connect the robot temporarily to the WiFi
    Use the command: wifi_cli -c "SSID" "password“
    You must reset the WiFi after you installed the custom firmware, otherwise Valetudo will not work!
  Connect your computer to the robot‘s WiFi, and run a local HTTP server on your computer
    Example: use python http.server or SimpleHTTPServer*
    * https://developer.mozilla.org/en-US/docs/Learn/Common_questions/set_up_a_local_testing_server
Depending on your device model and firmware version, this might not work

## Slide 34: Reset Method Step 7
Check this document: https://builder.dontvacuum.me/dreame/cmds-reset.txt
Make sure that your robot is fully charged and back in its dock
Run this commands to download an install the rooted firmware:
  cd /tmp
  wget --no-check-certificate {url-of-firmware.tar.gz}
  tar -xzvf {name-of-firmware.tar.gz}
  ./install.sh

## Slide 35: UART Method
Only for 1C/F9/D9
Do not use this method if the Reset method works for you!

## Slide 36: UART method
You can find all commands and steps in a text file here:
  https://builder.dontvacuum.me/dreame/cmds.txt
  It is recommended that you copy+paste the commands (instead of typing them)
Idea: Interrupt U-Boot, boot in single user mode, backup files
Limitation: works only on 1C/F9/D9
Power off the robot
Connect to UART (115200 baud, no flow control)
Power on the robot and keep key “s” pressed
Modify the command line and boot
Print files over UART
Install custom firmware

## Slide 37: UART Method Step 1
Get an adapter
Reminder: Works only on 1C/F9/D9
UART-USB adapter (3.3V, aka TTL adapter)
  Typical chipsets:
    FT232RL, FT232, PL2303TA or CP2102
  Price ~10 USD/Euro
Notes: To root the devices we need a few tools. We need screwdrivers to disassemble the device. I created a step by step video about how to do that. Its linked in the description.
Also we need a UART to USB adapter. You might find them under various names, like serial adapters or TTL adapters. The important thing here is that they support 3.3V logic level. Usually you can get them very cheaply over amazon or even in local stores.
For the actual connection, we need a few thing isolated copper wires or some breadboard jumper wires. Also some tape might be helpful.

## Slide 38: UART Method Step 2a
Know where RX and TX on your adapter is
Configure your UART program
  Baud: 115200
  Flow control: off (!)
Test the settings without robot
Notes: In this step, we want to setup your computer for the serial connection. You need to know where the RX and TX on your adapter is. For some adapters its marked, for some it’s a particular color of cable. In my case white was RX and green was TX. But don’t worry, you cant damage your robot, if you have it wrong.
Set your UART program to 115200 baud and disable flow control. This is very important. I have shown here a few example programs. Finally you want to test your settings. If you connect TX and RX of your adapter together and then type something, you should see an echo. This is what we call loopback.

## Slide 39: UART Method Step 2b
Connect serial wires to PCB
  Do not connect 5V (red cable)!
  Test for correct connection
    Press middle button (<1s)
    You should see some output
Notes: In the next step, we connect to the robot. First, we need to connect the battery to the PCB. There is only one way to connect it, so you should not be able to do it wrong.
Then we connect the serial wires to the PCB. As mentioned before, you can use a MicroUSB cable to get ground. Connect TX and RX. Do not connect the red cable which is 5V. This is very important.
As a first test, that you did everything correctly, press the power button less than one second. It’s the middle button on the PCB. If you do that, you should see some text output from your robot. If you don’t see anything, then you might have mixed RX and TX or your connection is bad. If you see some cryptic text, your settings might be incorrect.

## Slide 40: UART Method Step 3
Inside the terminal program
  Hold “s” key on your keyboard
  At the same time: Press middle button for 3 seconds
  We want to see this:
Notes: Now comes the important part. Press and hold the S key on your computer. Then at the same time press the middle button for 3 seconds. You should see some text and at some point you should have the prompt of the bootloader.
If you don’t see that prompt and you see Ubuntu booting instead, you might have forgotten to disable flow control in your serial terminal.

## Slide 41: UART Method Step 4a
In the U-Boot shell run this commands:
  setenv init /bin/sh
  setenv boot_partition boot1
  run setargs_nand
  run boot_normal
Your robot should boot and present you a shell

## Slide 42: UART Method Step 4b
After the system booted, run these commands (copy+paste from the cmds.txt):
  /etc/init.d/sysconfig.sh
  echo V > /dev/watchdog
  /etc/init.d/mount_private.sh
  /etc/init.d/mount_misc.sh
  mount /tmp
  mkdir /tmp/fakeetc
  cp -R /etc/* /tmp/fakeetc
  mount --bind /tmp/fakeetc /etc
  echo >> /tmp/fakeetc/inittab
  echo '::respawn:-/bin/sh' >> /tmp/fakeetc/inittab
  exec init

## Slide 43: UART Method Step 4c
Run these commands to print the configuration (save output):
  grep "" /mnt/private/ULI/factory/*
Run these commands to save the calibration (save output):
  grep "" /mnt/misc/*.json
  grep "" /mnt/misc/*.yaml
  cat /mnt/misc/*.txt
  hexdump /mnt/misc/*.bin
Some files might not exist on your device. That is normal.
Make sure that you copy the full output to a text file and save it

## Slide 44: UART Method Step 5
Check this document: https://builder.dontvacuum.me/dreame/cmds.txt
Make copies of the firmware encryption keys (e.g., to restore the robot to a factory state)
  cat /etc/OTA_Key_pub.pem
  cat /etc/publickey.pem
Make sure that you save the output of the calibration and the encryption keys before proceeding
Run these commands to create binary backups:
  mkdir -p /tmp/backup
  tar -cvzf /tmp/backup/misc_backup.tgz -C /mnt/misc .
  tar -cvzf /tmp/backup/factory.tgz -C /mnt/private/ULI/factory/ .
  cp /tmp/backup/*.tgz /data/

## Slide 45: UART Method Step 6
Check this document: https://builder.dontvacuum.me/dreame/cmds.txt
If the robot is already in your WiFi, skip this step
If the robot is still unprovisioned, you have 2 choices
  Connect the robot temporarily to the WiFi
    Use the command: wifi_cli -c "SSID" "password“
    You must reset the WiFi after you installed the custom firmware, otherwise Valetudo will not work!
  Connect your computer to the robot‘s WiFi, and run a local HTTP server on your computer
    Example: use python http.server or SimpleHTTPServer*
    * https://developer.mozilla.org/en-US/docs/Learn/Common_questions/set_up_a_local_testing_server
Depending on your device model and firmware version, this might not work

## Slide 46: UART Method Step 7
Check this document: https://builder.dontvacuum.me/dreame/cmds.txt
Make sure that your robot is fully charged and back in its dock
Run this commands to download an install the rooted firmware:
  cd /tmp
  wget --no-check-certificate {url-of-firmware.tar.gz}
  tar -xzvf {name-of-firmware.tar.gz}
  ./install.sh

## Slide 47: Livesuit/FEL rooting
This method is our fallback method in case the other methods do not work. There is more risk involved. Before you use it, please ask us.

## Slide 48: For 1C/F9/D9 only: DO NOT PROCEED if you do not have a backup of the configuration and calibration!! (check the method at the end of this pdf document)
Please report any issues directly (e.g. misflash, non-booting, etc)

## Slide 49: Root Step 1
Make sure that the robot is not connected over USB
Open Phoenixsuit and select image

## Slide 50: Root Step 2
Boot the Robot in FEL mode
  Connect MicroUSB to your computer (no USB hub, preferred USB 2.0 port)
  Connect BOOT_SEL to GND
    Use jumper wire (see 2a)
    Basic adapter (see 2b)
    Advanced adapter (see 2c)
  Press the power button for 3 seconds
    USB device should show up on your computer
    You might need to install the Phoenixsuit drivers located in “Drivers/AW_Driver”
      (via Device Manager -> Unknown Device -> Update drivers)
      If that does not work, download it here: https://builder.dontvacuum.me/usbdriver.zip

## Slide 51: Root Step 2a
Jumper wires: Ideally you have 2mm headers
  Make sure that the USB connection stays stable before you trigger the update (check the Windows Device Manager)
  2.54 pitch jumper cables might fit but can cause issues

## Slide 52: Root Step 2b
Basic PCB: Short the left pin to GND (e.g. with screwdriver)

## Slide 53: Root Step 2c
Advanced PCB: Short BOOT_SEL pads
BOOT_SEL

## Slide 54: Root Step 3
Disconnect BOOT_SEL before proceeding
In Phoenixsuit
  Click on Update
  If asked about mandatory format, select “No” !
  Wait for Update to finish

## Slide 55: Root Step 3 Trouble shooting
Do not use USB hubs
Use only USB 2.0 connections
If the device is detected initially, but disappears:
  Try to use a different USB port
  If you use VMs: Make sure that the USB filter is correct

## Slide 56: Firmware customization

## Slide 57
You have now installed a custom firmware ;)

## Slide 58: Customization of firmware
The firmware builder adds to hooks to the start process
  /data/_root_sysconfig.sh (gets executed early)
  /data/_root_postboot.sh (gets executed after boot)
At each boot we check for the presence of the custom files
  Safety measurement: In case something goes wrong, a factory reset will delete this files
An example file can be found in /misc

## Slide 59: Valetudo installation
Download valetudo binary to /data:
  https://github.com/Hypfer/Valetudo/releases
  Device dependent (check our website):
    1C, F9, D9: valetudo-armv7-lowmem
    1T, L10 Pro: valetudo-aarch64
  “wget https://github.com/Hypfer/Valetudo/releases/latest/download/valetudo-armv7-lowmem -O /data/valetudo”
Make valetudo executable
  “chmod +x /data/valetudo”
Enable boot script
  “cp /misc/_root_postboot.sh.tpl /data/_root_postboot.sh”
  “chmod +x /data/_root_postboot.sh”
Reboot
Check https://builder.dontvacuum.me/dreame/cmds.txt for a copy-pastable command list
You might need to add “--no-check-certificate” if wget fails

## Slide 60
Thank you for watching!
@dgi_DE
Website: dontvacuum.me

## Slide 61: Backups via UART
Only relevant if you have a 1C/F9/D9 and Reset method does not work

## Slide 62: Backup of configuration and calibration
Background: If flashing the custom firmware fails, the robot might delete the configuration and calibration files
Idea: Interrupt U-Boot, boot in single user mode, backup files
Limitation: works only on 1C/F9/D9
Power off the robot
Connect to UART (115200 baud, no flow control)
Power on the robot and keep key “s” pressed
Modify the command line and boot
Print files over UART

## Slide 63: Backup Step 1
Get an adapter
Reminder: Works only on 1C/F9/D9
UART-USB adapter (3.3V, aka TTL adapter)
  Typical chipsets:
    FT232RL, FT232, PL2303TA or CP2102
  Price ~10 USD/Euro
Notes: To root the devices we need a few tools. We need screwdrivers to disassemble the device. I created a step by step video about how to do that. Its linked in the description.
Also we need a UART to USB adapter. You might find them under various names, like serial adapters or TTL adapters. The important thing here is that they support 3.3V logic level. Usually you can get them very cheaply over amazon or even in local stores.
For the actual connection, we need a few thing isolated copper wires or some breadboard jumper wires. Also some tape might be helpful.

## Slide 64: Backup Step 2a
Know where RX and TX on your adapter is
Configure your UART program
  Baud: 115200
  Flow control: off (!)
Test the settings without robot
Notes: In this step, we want to setup your computer for the serial connection. You need to know where the RX and TX on your adapter is. For some adapters its marked, for some it’s a particular color of cable. In my case white was RX and green was TX. But don’t worry, you cant damage your robot, if you have it wrong.
Set your UART program to 115200 baud and disable flow control. This is very important. I have shown here a few example programs. Finally you want to test your settings. If you connect TX and RX of your adapter together and then type something, you should see an echo. This is what we call loopback.

## Slide 65: Backup Step 2b
Connect serial wires to PCB
  Do not connect 5V (red cable)!
  Test for correct connection
    Press middle button (<1s)
    You should see some output
Notes: In the next step, we connect to the robot. First, we need to connect the battery to the PCB. There is only one way to connect it, so you should not be able to do it wrong.
Then we connect the serial wires to the PCB. As mentioned before, you can use a MicroUSB cable to get ground. Connect TX and RX. Do not connect the red cable which is 5V. This is very important.
As a first test, that you did everything correctly, press the power button less than one second. It’s the middle button on the PCB. If you do that, you should see some text output from your robot. If you don’t see anything, then you might have mixed RX and TX or your connection is bad. If you see some cryptic text, your settings might be incorrect.

## Slide 66: Backup Step 3
Inside the terminal program
  Hold “s” key on your keyboard
  At the same time: Press middle button for 3 seconds
  We want to see this:
Notes: Now comes the important part. Press and hold the S key on your computer. Then at the same time press the middle button for 3 seconds. You should see some text and at some point you should have the prompt of the bootloader.
If you don’t see that prompt and you see Ubuntu booting instead, you might have forgotten to disable flow control in your serial terminal.

## Slide 67: Backup Step 4a
In the U-Boot shell run this commands:
  setenv init /bin/sh
  setenv boot_partition boot1
  run setargs_nand
  run boot_normal
Your robot should boot and present you a shell
Check https://builder.dontvacuum.me/dreame/cmds.txt for a copy-pastable command list

## Slide 68: Backup Step 4b
After the system booted, run these commands:
  /etc/init.d/sysconfig.sh
  echo V > /dev/watchdog
  /etc/init.d/mount_private.sh
  /etc/init.d/mount_misc.sh
Check https://builder.dontvacuum.me/dreame/cmds.txt for a copy-pastable command list

## Slide 69: Backup Step 4c
Run these commands to print the configuration (save output):
  grep "" /mnt/private/ULI/factory/*
Run these commands to save the calibration (save output):
  grep "" /mnt/misc/*.json
  grep "" /mnt/misc/*.yaml
  cat /mnt/misc/*.txt
  hexdump /mnt/misc/*.bin
Some files might not exist on your device. That is normal.
Make sure that you copy the full output to a text file and save it
Check https://builder.dontvacuum.me/dreame/cmds.txt for a copy-pastable command list

## Slide 70: Rooting preparations
Fully charge your vacuum robot
Required software: Phoenixsuit
  Download it here:
    https://androidmtk.com/download-phoenixsuit
Generate a custom firmware
  Go here:
    https://builder.dontvacuum.me/
    Select your model
    Fill out the form
    Select “Patch DNS” if you plan to use Valetudo (this disables the cloud)
    Use voucher “dreameroot”
    Select Livesuit image

## Slide 71: Alternative Method for 1C/F9/D9
You can root your device via UART
  Method might be safer
  Risk of soft-bricking reduced
  Check this link: https://gist.github.com/stek29/5c44244ae190f3757a785f432536c22a
  You need to build a normal firmware update (non-livesuit)
  Hint: Your robot must be docked and charged before you run the installer!